## Slide 1: 21 cm cosmology and the BINGO radio telescope
Carlos Alexandre Wuensche
on behalf of the BINGO Collaboration
ca.wuensche@inpe.br
August 31, 2021

## Slide 2: Plan of the lectures
21 cm cosmology
21 cm observations
the BINGO project

## Slide 3: The BINGO Telescope BAOs from Integrated Neutral Gas Observations

## Slide 4: BINGO - BAOs in Integrated Neutral Gas Observations
Visit us at https://bingotelescope.org

## Slide 5: Our sponsors

## Slide 6: Project management status (September 2021)
Most of the funding (> 60%) is already granted
  FAPESP: main funding agency.
  General coordination: Elcio Abdalla (IF/USP)
  Management team: C. A. Wuensche (INPE), Luciano Barosi (UFCG), Filipe Abdalla (UCL), Bin Wang (YangZhou Univ.)
BINGO construction proceeds…
  Major Project Review 2019  green light to proceed to Phase 2.
  Road work and site preparation started January 2021
  Horn, transitions, polarizer, and magic tee prototypes successfully tested (2018 – 2021)
  Main receiver components (first stage LNAs and filters, secondary LNAs and filters) qualified (2020 – 2021)
  Receiver undergoing tests and integration to the digital backend at INPE
  First horn prototype coupled to a simple radiometer currently looking at the sky in Paraíba
  Optical design completed (2021)
  Engineering projects near completion
  Dish fabrication under discussion

## Slide 7: The BINGO main science case
Measure BAOs on top of the 21 cm Hydrogen spectrum => intensity mapping in radio
Redshift interval BINGO will reach starts right after DE starts dominating the Universe => possible to set constraints on its properties
HI intensity mapping can be used as mass tracer, probing distortions in redshift space
Complementary to large optical surveys
Notes: Acoustic waves imprinted on CMB 380,000 years after Big Bang
Acoustic scale D set by distance light travelled at that time
  Known precisely from CMB power spectrum
  D=147.4 ± 0.6 Mpc (from Planck results)
BAO scale imprinted on all matter in the Universe
  Use as a “standard ruler”
Baryon oscillations seen in the CMB distribution can be observed in the spatial distribution of galaxies
The acoustic peak gives the ratio of the distances to z=.35 and z=1,100 to 4% fractional accuracy.
Absolute distance to z=0.35 is determined to 5% accuracy.
Co-moving sound horizon scale 149 h-1 Mpc

## Slide 8: Additional science with BINGO
BAOs contain additional information about
  Matter density
  Redshift distortions
  Anisotropic BAOs…
Life history of hydrogen
Radio recombination lines
Galactic continuum
And, of course, FRBs, which will be delivered for free due to the nature of BINGO observational strategy
(We are building an ultra-deep large-area spectral survey at 980-1260 MHz)

## Slide 9: A survey of current and future experiments…
Source: The BINGO Collaboration

## Slide 10: Sky coverage
Source: The BINGO Collaboration

## Slide 11
LSST Cosmology map
LSST Cosmology map (simulated). arXiv:1708.04058, chap. 9, fig. 9.3.
BINGO coverage area in white

## Slide 12
General BINGO pipeline information flow
From E. Merícia

## Slide 13: Challenges (October 2021)
Large telescope: discussions ongoing with the company to produce the dishes
Large horns: fabrication process understood, discussions ongoing with the company to produce the horns
Calibration and stability: use colfets and a CW source as internal calibration. Noise and stability for both are under investigation
Receiver stability: has to be tested with internal cooling and later, under the hot environment temperature in Paraíba
Digital backend: SKARAB boards are the choice. Learning curve for their programming is not known yet, need to be integrated to the system in the lab
Optical design: optics simulations indicate very small distortions of the beams for the current horn array. Final horn positioning still to be determined. TBC during commissioning
Radio Frequency Interference  Mobile quiet zone has been already requested to the state authorities (both to State agencies and to ANATEL)

## Slide 14
Accepted for publication - A&A
Replying to the referee - A&A

## Slide 15
FRB
Bispectrum
Minkowski functionals
E. Abdalla et al. arXiv:2107.01633

## Slide 16
C. A. Wuensche et al. arXiv:2107.01634

## Slide 17: The “FIDUCIAL” BINGO – Phase 1 (June 2021)
RECEIVER INFORMATION | 
T_sys (K) | 70
Minimum frequency (MHz) | 980
Maximum frequency (MHz) | 1260
Frequency band (for 30 channels, MHz) | 9.33
Instrument noise (mK, 1 second) | 26.5
Instrument noise (mK, 1 second) | 26.5
Digital backend FFT channels | 2048
Sampling time (s) | 0.1
SURVEY INFORMATION | 
Beam resolution (FWHM, deg.) | 0.67
Total covered area (sqr deg) | 5300
TELESCOPE INFORMATION | 
Site coordinates (vertex of the area) | 
7° 2' 27,6" S | 38° 16' 4.8" W
Site denomination: Serra da Catarina, Aguiar (PB) | 
Focal length (m) | 63.2
Primary major semi-axis (m) | 25.7
Primary minor semi-axis (m) | 20.0
Secondary major semi-axis (m) | 18.3
Secondary minor semi-axis (m) | 18.0
Primary area (m2) | 1620
Effective area (average, m2) | 600
Number of horns | 28
Telescope orientation | N-S
Central declination (deg.) | -15
Fixed wire-mesh parabolas
No moving parts
Transit telescope
Most components “off-the-shelf”
Guiding principle : simplicity !

## Slide 18
V. Liccardo et al. arXiv:2107.01636

## Slide 19
A. A. Costa et al. arXiv:2107.01639
Notes: Fig. 12. 68% and 95% CL marginalized constraints for two interacting dark energy models with
Q proporcional a RHO_de and w < - 1 (top)
Q proporcional a RHO_dm (bottom)

## Slide 20
J. Zhnag et al. arXiv:2107.01638
Notes: Fig. 18. We show the angular power spectrum of HOD mocks (solid faint curves) comparing to the calculation of UCLCl code with linear calculation (dashed lines) and halofit nonlinear correction (dotted lines) in redshift space.
Red (orange, green, blue) lines show the result from 960 (1050, 1150, 1160) MHz to 970 (1060, 1160, 1260) MHz, middled at 965 (1055, 1155, 1255) MHz, which are amplified by 0.25 (0.5, 1, 2) times for better illustration.
HOD mock measurements are higher than the linear calculation, but lower than the halofit calculation at small scale.

## Slide 21
F. Abdalla et al. arXiv:2107.01635

## Slide 22
K. Fornazier et al. arXiv:2107.01637

## Slide 23: Forthcoming papers
FRB data analysis (led by Marcelo Novaes)
Estimation of sensitivity to BAO signal (led by Camila Novaes)
Refining of foreground separation methods (led by Eduardo Mericia)
The BINGO receiver (led by Fred Vieira)
Cross-correlations with optical surveys
Other works in progress

## Slide 24
Thank you!
Visit us at http://www.bingotelescope.org

## Slide 25: NEXT STEPS

## Slide 26: The BINGO location
Paraíba state

## Slide 27
Serra da Catarina, Vale do Piancó (PB)
7° 2' 27,6" S; 38° 16' 4.8" W
Photo: M. Peel

## Slide 28
Status as of March 01, 2021

## Slide 29: Artistic view – May 2021

## Slide 30: The BINGO subsystems

## Slide 31: Receiver prototype
Led by CAW

## Slide 32
Notes: The nominal BINGO receiver layout. A correlation receiver is used to amplfy the signals from a horn and a COLFET (acting as a reference signal). The horn, polarizers and first hybrid (magc tee) are shown more clearly in Fig. 3.1.

## Slide 33: Receiver status
Desired: full orrelation receiver
Photo: M. Peel @ INPE’s lab
Notes: The nominal BINGO receiver layout. A correlation receiver is used to amplfy the signals from a horn and a COLFET (acting as a reference signal). The horn, polarizers and first hybrid (magc tee) are shown more clearly in Fig. 3.1.

## Slide 34
Horn & polarimeter status
Aluminum horns
  6060 T4 alloy
  Mass: ~ 400 kg
  Number of rings (sectors): 127
  Length: 4318 mm
  Mouth: 1900 mm
  Throat: 250 mm
Prototype construction
  Calfer (Brazil)
Polarimeters transitions and magic tees (aluminum)
  Mass: ~ 90kg,
Prototype construction
  Metalcard (Brazil)
EM project: Bruno Maffei (IAP, France)
  Contributions from Chris Radcliffe (Phase 2 Microwave, UK)
Mechanical project : Luiz Reitano (INPE, Brazil)

## Slide 35: Horn testing results –polarization
900 MHz
1300 MHz
VERTICAL
HORIZONTAL

## Slide 36: Horn testing results – Combination of all freqs.
Vertical polarization
Horizontal polarization
Wuensche et al. (arXiv:1911.13188)

## Slide 37: Horn testing results
Chart: Frequency (MHz)
| 900 | 925 | 950 | 975 | 1000 | 1025 | 1050 | 1075 | 1100 | 1125 | 1150 | 1175 | 1200 | 1225 | 1250 | 1275 | 1300
H-pol | 21.68 | 22.08 | 22.39 | 22.68 | 23.05 | 23.25 | 23.49 | 23.65 | 23.93 | 24.18 | 24.34 | 24.51 | 24.7 | 24.79 | 25.21 | 25.38 | 25.65
V-pol | 22.07 | 22.62 | 22.73 | 22.74 | 23.02 | 23.19 | 23.5 | 23.66 | 23.89 | 24.18 | 24.38 | 24.58 | 24.64 | 24.75 | 24.89 | 25.07 | 25.3
Chart: Frequency (MHz)
| 900 | 925 | 950 | 975 | 1000 | 1025 | 1050 | 1075 | 1100 | 1125 | 1150 | 1175 | 1200 | 1225 | 1250 | 1275 | 1300
H-pol | 15.61 | 15.18 | 14.64 | 14.21 | 13.83 | 13.39 | 13.13 | 12.89 | 12.42 | 11.99 | 11.77 | 11.47 | 11.09 | 11.1 | 10.31 | 10.31 | 9.99
V-pol | 14.99 | 14.4 | 13.37 | 13.96 | 13.52 | 13.26 | 12.88 | 12.82 | 12.37 | 11.91 | 11.65 | 11.42 | 11.09 | 11 | 10.59 | 10.36 | 10.1
Chart: Frequency (MHz)
| 900 | 925 | 950 | 975 | 1000 | 1025 | 1050 | 1075 | 1100 | 1125 | 1150 | 1175 | 1200 | 1225 | 1250 | 1275 | 1300
H-pol | 46.01 | 54.19 | 46.95 | 50.15 | 51.73 | 53.01 | 54.23 | 48.39 | 58.19 | 48.7 | 72.78 | 60.3 | 57.21 | 58.99 | 56.12 | 56.17 | 56.36
V-pol | 49.7 | 62.83 | 56.17 | 51.92 | 64.65 | 57.29 | 57.23 | 55.54 | 56.15 | 54.22 | 55.39 | 60.51 | 63.6 | 60.34 | 57.07 | 59.44 | 59.69
Wuensche et al. (arXiv:1911.13188)

## Slide 38: Optical design
Coordinated by F. Abdalla, with original work from B. Maffei and I. Ferreira

## Slide 39: Sketch of 3-D model of optics
Source: BINGO Collaboration
Horn array
(detectors)
Primary mirror
Secondary mirror
Lat: -7 deg

## Slide 41: Primary dish
Source: Ponto de Apoio Engenharia

## Slide 42: Secondary dish
Source: Ponto de Apoio Engenharia

## Slide 43
Source: BINGO Collaboration (L. A. Reitano)

## Slide 44
Source: Ponto de Apoio Engenharia

## Slide 45: Focal plane – 28 horns
Declination coverage: ~ 15.4 deg
Future upgrade to 56 horns

## Slide 46
Abdalla, Marins, Mota et al., submitted to A&A

## Slide 47
Liccardo et al., submitted to A&A

## Slide 48: Data Analysis
Led by F. Abdalla

## Slide 49: Foreground budget
From Battye et al. (2013), still valid for the current BINGO configuration

## Slide 50
Fornazier et al., in preparation
Liccardo et al., in preparation

## Slide 51: Component separation
From K. Fornazier

## Slide 52
BINGO simulated input map @ 1100 MHz
BINGO reconstructed map @ 1100 MHz
Residuals
mK
From V. Liccardo
Notes: BINGO \textsc{Hi} plus noise maps with a Galactic mask applied at $\approx$ 1.1 GHz. In the $top$ panel, we have the input map, in the $middle$ panel, the GNILC reconstructed map and in the $bottom$ panel the residuals map (temperatures are given in mK).

## Slide 53: Fast Radio Bursts
Led by R. Landim, M . Vargas, A. Queiróz and and F. Vieira

## Slide 54: Fast Radio Bursts detection
FRB is not BINGO main science, but serendipitous detections are expected
Outriggers for interferometric pinpoint of the progenitor are being planned
Need ADDITIONAL FUNDING!
BINGO
Luo et al., arXiv:2003.04848
F. Vieira: estimates for BINGO
M.Sc. thesis from F. Vieira (2020) presented a preliminary analysis performance regarding FRB detections
For ~ 3 Jy (max flux density) BINGO will likely see about 1 event every 2.84 days…

## Slide 55: RFI Concerns
Led by L. Barosi

## Slide 56: The BINGO site in Paraíba is CLEAN in the radio band

## Slide 57
For comparison, the spectrum in the same band in Bleien Observatory (Switzerland)…

## Slide 58: Still, there are concerns about airplane coverage and geostationary satellites…
Peel, Wuensche et al (J. Astr. Instrumentation 2019)
Harper & Dickinson, arXiv:1803.06314v2

## Slide 59: And GNSS…
White lines: no GNSS closer than 29 deg. of the main be beam axias
GNSS in the beam of the telescope
Black dashed lines: L5 (1164 MHz) and
L2 bands (1260 MHz)
Yellow band (zoom and scale) to show the off-band leakage of GNNS into the band
Harper & Dickinson, arXiv:1803.06314v2

## Slide 60: Silence zone proposal (discussions with Anatel started October 2018)
ZONA 1: 500m - Telescope only
ZONA 2: 2km – Industrial activities, power plants (wind or solar), radios, wireless networks, radio repeaters
ZONA 3: 10km – No new ERB (only one now)
ZONA4: 25km – Keep current mobile antennas, new antennas can be installed upon request & approval. No wind or solar plants.
Source: L. Barosi

## Slide 62
http://www.personal.psu.edu/duj13/ASTRO545/

## Slide 63
From B. Maffei / I. Ferreira

## Slide 64
Abdalla, Marins, Mota et al., in preparation
BINGO beams measured @ LIT
Horizontal
polarization
Vertical polarization

## Slide 65
Abdalla, Marins, Mota et al., in preparation

## Slide 66: Projeto Arquitetônico – Outubro 2020

## Slide 68
Standard Cosmological Model
Observational tests
SN Ia
Weak
Lensing
Geometry of the Universe (k=0)
CMB
Baryon Acoustic Oscillations
Cluster Counting

## Slide 70
Peel et al, J. Astron. Instrum. (2019)

## Slide 71
Produção:L. Barosi

## Slide 72
From A. P. Souza

## Slide 75: Projeto Arquitetônico – Outubro 2020

## Slide 76
From L. Barosi